## Slide 1: 1.虚拟地址和物理地址的转换
知道VA所对应PA有什么好处呢
-在没有代码的情况下可通过MS TV TOOL dump出内存的资料

## Slide 3
BAVA 转换函数定义: \kernel\mstar2\hal\k6lite\cpu\include\mach\memory.h
#define _phys_to_virt(phys)
#define _virt_to_phys(virt) 转换伪代码如下：
PHYS_OFFSET
  --The physical address of the start of the memory
  0X20200000
PAGE_OFFSE
--The virtual address of the start of the kernel image
0XC0000000
  0X2020000
0XC000000

## Slide 4
LX1 和LX2地址映射
Security Level: Confidential A
CPU
LX1
Kernel space
User space
1G
3G
LX2
LX1
LX2
0x0000000
0xC000000
0xC080000
0xFFFFFFF
0x20000000
0x20200000
0x20280000
0xA0000000

## Slide 5: 虚拟地址、物理地址、实际内存的对应关系
Security Level: Confidential A
CPU
MIU0
DRAM
Kernel space
User space
1G
3G
MIU1
PA (51)
VA
BA
0x0000000
0xC000000
0xC080000
0xFFFFFFF
0xA0000000
0x00280000
0x20200000
0x20000000
0x20280000
0x00200000
0x00000000
Notes: 总线地址：是从外设看到的地址，如power pc、x86等，访问外设io有专门的指令
但是arm对外设和ram统一编址，所以总线地址等于物理地址，但是linux中为了兼容保留了这个概念
总线地址举例：比如有些DMA访问外设，cpu看到DMA的地址是虚拟地址，但是DMA看外设的地址就是总线地址
注意：内核起来后，只要mmu初始化成功，cpu看到的地址都是虚拟地址

## Slide 6
内核虚拟地址layout
Notes: 1. vector: 重定向向量表，如中断向量表
2. fixmap： 固定映射区，一般用来分配大页内存
3. vmalloc: 虚拟内存申请的内存，前三个一般指高端内存
4. lowmen： 直接物理内存映射区，与RAM 1：1映射，就是我们的LX
5. modules: 内核模块空间，内核模块通过insmod命令加载，会动态的映射到这里
6. .text: 内核代码加载的地方
7. .init: 内核中的init段，就是定义时前面加init的代码段
8. .data: 数据区，一般存放已初始化全局变量和一些静态变量
9. .bss: 一般存放已初始化全局变量

## Slide 7: 2. 一些内存api介绍
__pa(vAddr)
  Make sure vAddr locates at lowmem:
__va(pAddr)
Runtime representation
Security Level: Confidential A
LX1
LX2
LX1
LX2
LX_MEM2’s PA head
The same

## Slide 8
Use devmem to verify (devmem use bus address, remember!!)
Use 51 to verify
Security Level: Confidential A

## Slide 9
Ioremap/iounmap
  将物理地址/RIU地址映射到虚拟地址
  在系统中是不能直接访问RIU的，必须要进行映射才能访问
Security Level: Confidential A
Notes: Mstar的RIU地址一般是0x1F000000,这地址一般芯片设置好就固定了
映射地址一般是0xFD000000

## Slide 10
RIU地址和虚拟地址的转换
If offset is 8 bit
  (Bank補兩個0)*2 + offset * 2
If offset is 16 bit
  (Bank補兩個0)*2 + offset * 4
Example
  Given 1CD71C
  Bank = 1CD7
  Offset = 0x1C
  8bit
    1CD700 * 2 + 1C *2 = 0x1f39AE38-----------------------------for Devmem
    1CD700 * 2 + 1C *2 = 0x(mstar_pm_base) + 39AE38-------for code
  16bit
    1CD700 * 2 + 0E *4 = 0x1f39AE38-----------------------------for Devmem
    1CD700 * 2 + 1C *2 = 0x(mstar_pm_base) + 39AE70-------for code
Security Level: Confidential A
Notes: 此处需要注意访问8位寄存器地址的情况

## Slide 11
Kmalloc v.s vmalloc
Most important thing is:
  Don’t forget to kfree/vfree memory after use.
Security Level: Confidential A

## Slide 12: 2. Devmem/tv tool的使用方法
Devmep主要是提供给driver开发人员，在应用层侦测内存地址中的数据变化，比如在debug console动态的检测内存中数据的正确性

## Slide 13
如何打开devmem的功能
Security Level: Confidential A

## Slide 14
可以先在kernel中定义个变量来测试
Security Level: Confidential A

## Slide 15
build完kernel后用命令从vmlinux里面查出定义的变量的虚拟地址
$ arm32-linux-gnu-nm vmlinux | grep"devmem"
c0c796a0 D devmem_example
进行地址转换VA->PA
phy addr = VA – 0xc0000000 + 0x20200000
= c0c796a0 – 0xc0000000 + 0x20200000
= 0x20E796A0
Security Level: Confidential A

## Slide 16
得到物理地址后就可以在控制台通过devmep dump读出数据了
读值方法 busybox devmem [ADDRESS] [LEN(bit)]
# busybox devmem 0x20E796A0
0x00001111
写值方法 busybox devmem LEN(bit) [ADDRESS] [VALUE]
# busybox devmem 0x20E796A0 16 0xabcd
# busybox devmem 0x20E796A0
0x0000ABCD
Security Level: Confidential A

## Slide 17
TV_Tool去dump DRAM数据
地址： 0x20E796A0 -0x20000000 = E796A0
Security Level: Confidential A
Notes: 前面讲过物理地址是从0x20000000开始的，对应dram 0x000000000的位置

## Slide 18: 一些有用的调试小技巧 在移植kernel的时候，一开始没有log打印 可以通过下面的方法来查看程序跑到哪里了
Security Level: Confidential A

## Slide 19
Security Level: Confidential A
arm-none-linux-gnueabi-nm vmlinux | grep gshow_line
c0924298 D gshow_line
TV_Tool去dump DRAM 使用 0x20 0000+ 924298

## Slide 20: Dump __log_buf的数据
arm-none-linux-gnueabi-nm vmlinux | grep __log_buf
c09d2d18 b __log_buf
TV_Tool去dump DRAM 使用 0x20 0000+ 9d2d18
Security Level: Confidential A

## Slide 21
将存下來的bin file 放到server並执行
strings [Bin file] >test.log
例如 #strings getdata.bin >test.log
執行結果
Security Level: Confidential A

## Slide 22: 3.在kernel中增加调试节点
一般在proc中增加一个调试node，然后通过echo输入不同的值，做对应的流程控制
输入不同值，控制程序执行不同的代码段
输入不同值，对打印的log进行控制

## Slide 24: 4.内存泄漏检测Kmemleak
这是kernel中原有的功能
这个功能主要用来检测内存泄漏
这个功能可以检测哪些内存泄漏
kmalloc/kzalloc, vmalloc, kmem_cache_alloc

## Slide 25: KmemLeak work flow

## Slide 26
如何打开kmemleak的功能CONFIG_DEBUG_KMEMLEAK in “Kernel hacking” has to be enabled

## Slide 27: 如果有打印log buffer超出则自己调整一下

## Slide 28: Kmemleak的一些命令
立即触发一次内存扫描:
# echo scan > /sys/kernel/debug/kmemleak
获取内存泄漏信息:
# cat /sys/kernel/debug/kmemleak
清空当前的内存泄漏信息:
# echo clear > /sys/kernel/debug/kmemleak
如果“/sys/kernel/debug/kmemleak” 不存在, 尝试mount debugfs
# mount -t debugfs nodev /sys/kernel/debug/

## Slide 29: 内存泄漏信息
You will see the kmemleak report format
Size = memory allocate size
Age = how long this memory exist in system

## Slide 30: Example

## Slide 31
Meminfo显示的内存信息Kmemory 4096 bytes X 10...

## Slide 32: 5.MIU and MIU protect
Miu：内存接口单元，我们对dram的访问都通过miu来进行

## Slide 33: MIU architecture
IP
G0
IP
G1
IP
G2
IP
G3
MIU 0
G0
G1
G2
G3
MIU 1
G0
G1
G2
G3
Path
Select
Mask
DRAM
Address Bus
Data Bus
DRAM
Address Bus
Data Bus
reg_miu_sel
Notes: 每个miu可以对4块内存区域进行保护

## Slide 34: MIU Protection Architecture
0x0000000
0x2100000
0x2102000
0x1700000
0x1702000
0x3100000
0x3102000
0x3200000
0x3202000
ID=0
ID=1
ID=2
MIU
1st
2nd
3rd
4th
Mheg5-Aeon
ADP-Aeon
HK51
MAD
MVD
…
…
Client ID
ID0
ID1
ID2
ID3
ID4
ID5
ID6
ID7
Block 0
Block 1
Block 2
Block 3
U32Start
U32End
ID=3
Notes: 被保护的区域，只有加到白名单中的client才允许访问，每块区域最多可以添加15个白名单

## Slide 35: MIU protect
MIU Protect
  Protect an area of ram to prevent all MIU clients but some specific clients to write it.
Architecture Introduce
  Hardware provide 4 blocks for MIU protection.
  Each protected ID correspond MIU client ID
  API:
    MDrv_MIU_Protect (U8 Blockx, U8 *ProtectId, U32 u32Start, U32 u32End, BOOLEAN bEnable)
    Blockx is regarded as block ID (0~3), protectId is regarded as protected client ID, U32Start & U32End are regarded as the start address and end address of protection region, bEnable is regarded as turning on/off MIU protect
      Protect start/end address unit is 8KB
      Associated code is referenced to drvMIU.c/.h
Bus addr

## Slide 36: 用tv tool对miu做protect

## Slide 37: 6.Kernel panic 跟踪
什么是kernel panic
就是操作系统检测到一个它无法处理的内部错误，然后打印出相应的log
Kernel panic description
Death location
Register Info
Notes: Kernel panic：发生在kernel空间的错误
Coredump：发生在用户空间的错误

## Slide 38
PC (program counter) kernel死的地方
LR (Link register) 返回地址
SP (stack pointer) 堆栈指针
R0~R10: 一般寄存器
Kernel panic description
Death location
Register Info

## Slide 39
首先我们得从vmlinux中找到pc的地址
PC: 0xc053f104
arm-none-linux-gnueabi-objdump -S vmlinux
Address
Instruction code
Assambly code
Notes: Display information from object <file(s)>.
-S, --source Intermix source code with disassembly
-l, --line-numbers Include line numbers and filenames in output

## Slide 40
Or you can view symbol and its VA mapping by
  arm-none-linux-gnueabi-nm -S vmlinux
  arm-none-linux-gnueabi-objdump -S vmlinux

## Slide 41
Kernel Panic status in Console
PC = Init_idle+0x88 = 0xc053f104
Address
Instruction code
PC is here
Memory violation
PC’s instruction code is here

## Slide 42
检查vmlinux和Kernel panic log是否匹配
vmlinux
Kernel panic log

## Slide 43
r3 = r1+0x15c (r3 comes from r1, so go check r1)
r1 = r4+0x16c (r1 comes from r4, so go check r4)
We observe that r4 hasn’t been modified for a long time.
r4 is a suspect, so go check r4’s address
Notes: R1+#348得出的值並非在 LX裡面，照理來說kernel只會在LX裡面去讀資料 (ldr r3, [r1, #348])?
所以是mboot在搬移kernel資料後，又去動到LX嗎
Load LX的東西不應該有問題，所以懷疑有人去踩?

## Slide 44
r4=c0a78c00
Seems like r4 is in the region of lowmem
We are dead at the time when mboot is finished. And swtiched hand to kernel Kernel must get the wrong address which is caused by Mboot!
Go check if mboot access kernel’s memory!

## Slide 45
STR ON flow
Kernel MMAP
U-Boot override Kernel’s address space

## Slide 46
Kernel died just after Mboot finished
Solution
  Mmap must prepare an buffer to Mboot!
  prom_meminit( ) [mstar2/drv/cpu/arm/generic/memory.c] (hardcode)